## Slide 1: Arterial haemodynamics and flow through a stenosis

## Slide 3
Peak Systolic Velocity
PSV cm/s
Notes: We use spectral doppler through a sample volume placed within the centre of the artery to take peak systolic velocity measurements (PSV) which is basically when the blood is moving at its fastest in the centre of the vessel, this is measured in cm/s. Many patient specific factors affect the absolute velocity- we don’t use “normal reference PSV values” to make any diagnosis on the arteries- so that’s why individual values don’t actually mean a great deal. However when it comes to looking at stenoses they are essential! Before going into more detail will explain blood flow

## Slide 4: Blood flow
Heart contraction= energy to force blood
Blood flow depends on:
Energy
Resistance to flow
Notes: blood moves through our arteries due to energy created by the contraction of the heart that forces the blood around.
Blood flow in the arteries depends on 2 factors: the energy available to drive blood flow and the resistance to flow presented by the vascular system

## Slide 5: Bernoulli
TOTAL FLUID ENERGY
Pressure energy
Kinetic energy
Gravitational potential energy
Notes: The scientist bernoulli showed that the total fluid energy, which gives rise to the flow is made of 3 parts
Pressure energy: pressure in the fluid due to the contraction of the heart
Kinetic energy: the fact that the fluid is a moving mass
Gravitational potential energy: ability of a volume of blood to do work due to the effect of gravity (equivalent to hydrostatic pressure)

## Slide 6
K P
K P= energy losses
Notes: When fluid flows through a tube with a narrowing- the fluid travels faster through the narrowed section (or stenosis) this means that kinetic energy increases and the potential or pressure energy falls. So the pressure it lower in the narrowed section. Beyond the narrowing, the reverse happens, kinetic energy decreases and is converted into pressure energy. This results in small amounts of energy losses. Through normal arteries, these energy losses are very small with pressure differences between the distal vessels and the aorta being only slight. However in the presence of significant arterial disease/stenosis- the pressure drops are greater than normal and this leads to reduce blood flow and tissue perfusion distally.

## Slide 7: Pouiseuilles equation
Pressure drop= flow x resistance
Resistance to flow= viscosityxlengthx8/πxradius4
Notes: Pouiseuilles demonstrates the relationship between flow, the pressure gradient along the tube and the size/dimension of a tube. The take home message from this is that the presence of arterial disease/stenosis can signficantly alter the resistance to flow with the reduction in vessel diameter having a major impact- as you can see how to the power of 4! So slight changes in size have a change impact

## Slide 8
Notes: Anyway- that’s the science of the blood flow- where do velocities come in? So a narrowing also leads to an increase in the velocities we see- so as you can see here the velocity goes from 26-324 and according to our criteria this velocity increase suggests the narrowing or stenosis is >90%, so pretty tight! I will just explain why the velocity increases and then explain our grading criteria

## Slide 9: Flow in a tube
Velocity = volume flow/area
V=Q/A
For a given constant volume flow, velocity varies inversely with area.
If area decreases=velocity increases (stenosis)
If area increases=velocity decreases (aneurysm)
Notes: But why does velocity increase? Back to bernoulli. Obviously blood flow is complex and we have discussed blood energy, this equation explains volume flow and velocity. Velocity(speed of the blood), volume of flow (amount of blood at that point) and cross sectional area of the tube are all linked by this equation. The volume flow remains constant (because flow cannot be created or destroyed through a tube, some changes at a branch/bifurcation), therefore velocity at any point along the tube is dependent on the area.

## Slide 10: Remember Pouiseuilles law
Resistance to flow= viscosityxlengthx8/πxradius4
Notes: This is complex but important just for one thing: flow is proportional to the 4th power of the radius (area) of the vessel, which tells us that even small changes in the radius or area of the vessel results in large changes in flow/velocity.

## Slide 11: At a stenosis
Pressure losses
Resistance increase
Velocity increases
PSV ratio: V1/V2
V1
V2
Notes: At a stenosis we have pressure losses, increase in resistance and increases in velocity- which is what we can measure, interpret and use to diagnose the degree of stenosis. The main PSV criterion used to grade the degree of stenosis in the artery is the ratio between the velocity at the site of the stenosis and the prestenotic velocity in a normal segment immediately proximal to the stenosis.

## Slide 12: Criteria for the estimation of stenosis
Diameter reduction | Velocity ratio
<50% not significant | <2
50-70% haemodynamically significant | 2-3.3
70-99% haemodynamically significant | 3.4≤
Near-occlusion | High, low – string flow
Occluded | No flow
Notes: Velocity criteria used to quantify the degree of narrowing have been produced by comparing Doppler velocity measurements with arteriogram results- which is/used to be considered the gold standard.
So lesions that take up <50% of the vessel lumen are non haemodynamically significant- they do not have much of an impact on velocity/resistance/pressure where as any stenosis 50% or over is deemed haemodynamically significant