## Slide 1: Clinical Vascular Scientists Who, where, how, what, when and why! Julia Warne
Vascular Laboratory
GHNHSFT

## Slide 2: Who are we?
8 Clinical Vascular Scientists
2 Trainee Vascular Scientists
3 Specialist Admin
Notes: Within the Vascular Lab of Gloucestershire Hospitals we have 8 clinical vascular scientists, 2 trainee Clinical Vascular Scientists completing the 3 year STP and 3 specialist admin staff.

## Slide 3: Where are we ?
CGH
GRH
West Block
Gallery Wing
Notes: . The majority of us rotate daily between the Labs on each site- GRH within the gallery wing and CGH in West block where we see a range of inpatients and outpatients from a range of specialities. Our core hours are Monday to Friday 8.30-4.30
Lab
We mostly get inpatients to us but can be portable=theatres, dcc, wards etc for various reasons

## Slide 4: How to become a vascular scientist?
Relevant BSc
Scientist Training Programme (STP)
3 years work based training with university blocks
1st year rotations
MSc Clinical Science
Clinical Vascular Scientist
Accreditation
min 3 years experience
1100 scans
3 exams
Notes: Following on from a relevant undergrad you apply for the scientist training programme which is a nationwide programme a wide range of healthcare science specialisms from cancer genomics and clinical microbiology to nuclear medicine and of course vascular science. If you are a successful applicants are employed by a Trust for 3 years for work based training with uni blocks, rotate through a range of relevant departments in the 1st year, and you complete an MSc in clinical science. s. Once the STP is complete we can gain statutory registration and become Clinical Vascular Scientist, then After completing min 3 years experience and 1100 scans across 4 modalities we can gain accreditation with the society of clinical vascular scientists
It is an intensive training and The royal college of surgeons recognises our training as comparable to ST5 level for medics.

## Slide 5: What is Vascular Science?
Define
Types of scan-use HCS ppt
Bread and butter vs weird and wonderful
Figures from Gem
Artery
Vein
Notes: Vascular science is the study of blood vessels, the arteries and veins and the blood flow using ultrasound. Within vascular science we look at vessels outside of the heart that are responsible for taking blood to and from different areas of the body. As vascular scientists we have detailed knowledge of the vascular anatomy and surrounding structures

## Slide 6: What is Vascular Science?
The Problem
The Cause
The problem
The cause
Notes: So where we fit in to the patient pathway, so a patient presents with a problem and we are referred the patient and are responsible to determine the underling cause or provide more information about the problem so it can be fixed, then we might see the patient again after treatment to check progress. So for example here is a leg ulcer, the problem, and we identify the underlying cause, in this case- peripheral arterial disease

## Slide 7: How?
Add video of scan?
Ultrasound
Hand held Doppler
Notes: And so how do we do this? Within our vascular labs we utilising our specialist skill with ultrasound to obtain still and real-time moving images of the blood vessels and blood flow throughout the body and also we use hand held Doppler ultrasound to sample pulses and record pressures, as a way of detecting and grading vascular disease

## Slide 8: Why Ultrasound?
Define
Types of scan-use HCS ppt
Bread and butter vs weird and wonderful
Figures from Gem
Non-invasive
Repeatable
Inexpensive
Safe
Notes: So what makes ultrasound so good- in the hands of an experienced operator there are lots of benefits of ultrasound, it is safe as doesn’t use any radiation, it is non-invasive (cold gel is the worse bit), the scans are highly and readily repeatable and relatively inexpensive. And really innovative as a modality too

## Slide 9: Duplex Ultrasound
B-mode
Colour Doppler
Spectral Doppler
Triplex Ultrasound
Notes: Often you may hear of our scans being referred to as Duplex Ultrasound but really we should be calling it triplex ultrasound because we utilise 3 modalities of ultrasound during each of our scans: the B-mode, colour Doppler and spectral

## Slide 10: Triplex Ultrasound
B-mode
Black and white anatomical image
Demonstrate presence of disease along arterial and vein walls
Diagnose and provide surveillance for aneurysms
abdominal aorta
liver
spine
Notes: Often you may hear of our scans being referred to as Duplex scans but really we should it triplex ultrasound because we utilise 3 main features of ultrasound, which I will now explore a little more-the first is the B-mode or gray scale

## Slide 11: Triplex Ultrasound
Colour Doppler
Functional map to form a
colour flow image
Displays presence or absence of
blood flow in arteries and veins
Displays direction and speed of
blood flow
Notes: Functional map on top of the B-mode demonstrating direction and speed of blood

## Slide 12: Ultrasound
Spectral Doppler
Pulse Wave Doppler waveforms recorded from blood vessels
Assess blood flow and changes in blood flow
Calculate velocity measurements to grade disease severity

## Slide 13: Why and when?
Carotid artery - Stroke
Abdominal artery – aortic aneurysms
Peripheral arterial disease
Upper limb arterial
Fistulas
Varicose veins
Ankle Brachial pressure index
Temporal artery
Transcranial
Deep vein thrombosis
Iliac vein stent
Malformations
Pseudoaneurysms
Stent surveillance
Graft surveillance
Vein mapping
Superficial vein thrombosis
Mesenteric ischaemia
Notes: So within the vascular lab we look at a huge variety of different arteries and veins around the body and assess the problems associated with them, so as vascular scientists we have extensive knowledge of simple and complex vascular disease processes, here are some examples, red on the left are the arteries, left is veins. The ones in bold we are going to explore in a bit more detail

## Slide 14: Why and when?
Aneurysm
A localised swelling of an artery which exceeds 50% of its normal diameter
Normal
Aneurysm
1.5cm
5.0cm
Notes: So why and when are we needed? An aneurysm is defined as a localised swelling of an artery which exceeds 50% of its normal diameter. So here the abdominal aorta is normal and measures 1.5cm. Here the abdominal aorta is aneurysmal and measures 5.0cm so requires 3 monthly surveillance. Aneurysms are usually asymptomatic until they are either rupturing or in imminent danger of doing so, and rupturing carries a high mortality rate (so when 5.5cm is reached- risk of this goes up) the majority are detected coincidentally through routine clinical examination or abdominal imaging, or if you are a male >65yo through the NAAASP programme. In the vascular lab we check for aneurysms, here is a normal abdominal aorta in B-mode, and here is an aneurysm= we can then carry out surveillance programmes, monitoring aneurysm growth until treatment is required.

## Slide 15
Normal
Aneurysm (AAA)
1.5cm
5.5cm
Spine
Vena cava
Bifurcation
Notes: The patient will lie on the couch and we will perform an initial sweep in TP in B-mode. This cineloop in B-mode and using a TP demonstrates a normal aorta and as the scan goes down you can see landmarks such as the spine and vena cava, plus the aorta bifurcates into the iliac vessels. Landmarks are vital in vascular ultrasound to correctly identify the target vessel. Explain in more detail: this is a B=-mode (gray scale) image of an abdominal aorta with a frozen image taken in longitudinal plane, using our calipers (the stars) we measure across the lumen of the vessel (the black area) from, the inner wall to inner wall to measure the diameter. The top US image demonstrates a normal aorta without aneurysmal, the bottom image demonstrates an aneurysmal abdominal aorta and at 5.5cm this patient has reached the threshold for intervention and we will flag this to the vascular consultants and they will be reviewed for surgery

## Slide 16: AAA
US image of EVAR + explain surveillance
5.5cm
Do nothing
Open repair
Endovascular Aneurysm Repair (EVAR)
Notes: The vascular team will review appropriateness for surgery= with the principle aim of surgery to exclude the aneurysm from the circulation, so will have a CT scan and with the MDT then work out if they will do anything atall, perform open repair or perform an EVAR by insertion of a synthetic graft inside the aneurysm sac which we can assess in the vascular lab as EVARs have high complication rate

## Slide 17
Endovascular Aneurysm Repair (EVAR)
Contrast enhanced ultrasound (CEUS)
Endoleak and increasing sac size
Notes: We perform yearly EVAR surveillance scans to check the stents and monitor the size of the residual aneurysm sac as endoleaks can form increasing the size. This patient was found to have an endoleak from a small lumbar artery which was causing the sac expand. To provide further information about the endoleak in the vascular lab we also can perform contrast enhanced ultrasound alongside the radiologists using bubbles created by the injected contrast to guide more precisely the type of endoleak and how the endoleak might be fixed- as shown on these images here

## Slide 18: Why and when?
Atherosclerosis
Cholesterol-laden fatty plaque building up within the lumen of arteries and reducing blood supply to target organs
Plaque
Notes: So another thing we are often asked to identify is Atherosclerosis is the most common form of vascular disease and is the build up of cholesterol-laden fatty plaque building up within the lumen of the arteries which significantly narrows by 50% or more or blocks the artery, this has a significant impact on blood flow reducing flow to the target organ, thus causing a range of associated symptoms

## Slide 19: Why and when?
Atherosclerosis
Carotid disease
Peripheral arterial disease
Reduced blood flow to the limbs
Intermittent claudication (IC)
Chronic Limb Threatening Ischaemia (CLTI)
Disruption of blood flow to the brain
Intermittent claudication (IC)
Chronic Limb Threatening Ischaemia (CLTI)
Transient Ischaemic Attack (TIA)
Cerebral Vascular Attack (CVA) or stroke
Notes: Atherosclerosis builds up within the carotid arteries of the neck, the main brain supply to the brain, causing disruption of flow and then TIA or CVA. Also atherosclerosis can cause peripheral arterial disease causing reduced blood flow to the limbs and symptoms such as IC and CLTI incorporates rest pain and tissue loss

## Slide 20: Carotid Artery Disease
Internal Carotid Artery
Internal Carotid Artery
External Carotid Artery
Common Carotid Artery
Common Carotid Artery
Vertebral artery
Vertebral artery
Subclavian artery
Subclavian artery
Brachiocephalic artery
Notes: Lets explore carotid disease in a little more detail. Here are all the vessels we look at during our routine carotid duplex scans- here is a B-mode image of the common carotid bifurcation- where it splits into the internal and external carotid arteries, this is the colour image of normal, non-diseased vessels

## Slide 21: Normal internal carotid artery waveform
Notes: WE also take spectral doppler waveforms from all the arteries

## Slide 22: Carotid Artery Disease
Common Carotid Artery
External Carotid Artery
Internal Carotid Artery
TIA clinic: 20 minutes of right sided weakness
Left hemisphere
Notes: So when atherosclerosis builds up in the carotid arteries, specifically the internal carotid artery, this can cause significant stenosis, here is how one looks on color Doppler- you can see the narrowed channel of flow and this will disrupts the blood flow to the brain and causes TIAs or strokes. When patients present with symptoms of TIA they are seen in the one stop TIA clinic and we perform a Carotid Duplex scan as part of this, this colour image is taken from a recent patient in the TIA clinic, who presented with 20 minutes of right sided weakness and had a left hemisphere TIA- just a reminder- the right side of the body is controlled by the left hemisphere of the brain which is supplied by the left ICA

## Slide 23
Notes: So as part of our Carotid Duplex assessment we look at the CCA using B-mode, colour and spectral Doppler and take some velocities. Here I can see nice colour filling to the walls and very little in the way of plaque, the PSV 50

## Slide 24
Notes: Then moved onto the ICA where things are a little different- on the colour image you can see a narrowed lumen and on the b-mode plaque has built up within the vessel- also on the spectral Doppler we have increased velocities at 485.

## Slide 25: Carotid Artery Disease
NASCET
485/50=9.7
Notes: So with all the information we generate a report, which demonstrates here that this patient has a symptomatic significant >90% stenosis of the left ICA. How have we determined this- alongside appearances on B-mode and colour, we use the velocities to calculate the degree of stenosis. So we need to get up our NASCET criteria- angiographically standardised stenosis grading criteria to guide our delineation of the stenosis- so firstly we take the ICA PSV which is 485- into this box, then usingthe CCA PSV we calculate a ratio- which is 9.7 so greater than 5 and that goes into this box and tells us this stenosis is likely ot be>(). The end column is used when there is ambuiguity with the other criteraia. So this patient has a significant, symptomatic internal carotid artery stenosis and needs vascular review.

## Slide 26: Carotid Artery Disease
Carotid endarterectomy
Best medical therapy
Hyperlipidemia
Hypertension
Diabetes
Smoking cessation
Notes: Each patient will be reviewed for lifestyle modifications and optimisation of medical therapy to minimise stroke risk. The review also involves determining if the patient is a suitable surgical candidate for carotid endarterectomy, with the primary aim to reduce the risk of further stroke. This patient went onto have surgical treatment in the form of carotid endarterectomy, where significant stenotic plaque is surgically removed from the internal carotid artery

## Slide 27: Peripheral Artery Disease
Popliteal Artery
Aorta
Common Iliac Artery
Common Femoral Artery
Superficial Femoral Artery
External Iliac Artery
Internal Iliac Artery
tibio-peroneal trunk
Posterior tibial artery
Anterior tibial artery
Peroneal artery
Inguinal ligament
Adductor canal
Profunda Femoris Artery
Notes: So during our routine assessment for peripheral arterial disease we can look at the arteries of the lower limb as shown here. For the scan we will get the patient to lie down on the couch and scan from their abdomens all the way down the inside of their thigh and the inside and outside of their calf and can take up to 45mins + reporting time. Here are some images taken from normal, non-diseased vessel. Here you can see the CFA and its bifurcation into the SFA and PFA, this colour flow image demonstrates filling to the walls and appearances are good, then follow the SFA down into the popliteal artery behind the knee.

## Slide 28: Peripheral Artery Disease
Diabetic foot ulcer
Notes: Lets have a look at a real life example a Patient with an infected diabetic foot ulcer, was seen in the vascular hot clinic and scanned the same day by us. The report demonstrates multi-level disease, starting at the CFA- We noted the waveforms were triphasic as indicated here suggesting there is no disease higher up so we didn’t need to scan their abdomen- the report demonstrates <50% so non-significant plaque which looks like this on the ultrasound.

## Slide 29
Notes: which looks like this on the ultrasound.

## Slide 30: Peripheral Artery Disease
Diabetic foot ulcer
Notes: Then within the proximal SFA there was ~50% stenosis which appeared as so on colour image

## Slide 31: Peripheral Artery Disease
Notes: Longitudinal

## Slide 32: Peripheral Artery Disease
Diabetic foot ulcer
Notes: The within the mid-thigh there is a signficant stenosis- these numbers are the recorded velocities, and the 70-99% indicates the severity of the disease, so pretty severe in this case. SO to determine this

## Slide 33
428/68=6.3
Notes: We took the PSV from the less diseased artery before and the PSV at the tightest point of the stenosis and divided them to generate a ratio

## Slide 34: Peripheral Artery Disease
428/68=6.3
Notes: Then like with the Carotid artery Duplex we use the information within our depattmental standard operating procedure and using the criteria can determine that based on the velocity ratio, the stenosis is 70-99%.

## Slide 35
Notes: Finally, we determine the posterior tibial artery is occluded or blocked and this is what it looked like on the US

## Slide 36
Notes: As was the anterior tibial artery

## Slide 37: Peripheral Artery Disease
Notes: However the peroneal artery was patent with monophasic flow
We see a huge range of disease states, no 2 patients are the same, and this patient

## Slide 38: Occlusive disease
Notes: Has severe occlusive disease and probably has sx of CLTI and the US imagefrom the SFA

## Slide 39: Peripheral Artery Disease
Treatment
Best Medical Therapy + lifestyle advice
Endovascular revascularisation
Open revascularisation
Amputation
Notes: Best medical therapy is offered to all PAD patients alongside lifestyle advice, smoking cessation etc.
Then endovascular revascularisation options are explored such as angioplasty and stenting which are a minimally invasive approach and involves a image guided technique where is wire is threaded through the blockage and devices such as balloons and stents are passed over the wire and used to re-open the blocked or narrowed artery

## Slide 40: Angioplasty+/- stenting
Notes: which are a minimally invasive approach and involves a image guided technique where is wire is threaded through the blockage and devices such as balloons and stents are passed over the wire and used to re-open the blocked or narrowed artery. Here are some angiographic images from a patient having an angioplasty and then a stent deployed. Stents are metal mesh tubes and we can see them on ultrasound and these patients are then refered to us to check how well these procedures go and this example here you can see the bright, cross-hatched walls of the stent within the SFA that has created a uniform channel of flow in a previously blocked artery. We provide surveillance with regular scans to improve the durability of the stents on a case-by case preference

## Slide 41: Peripheral Artery Disease
Treatment
Best Medical Therapy + lifestyle advice
Endovascular revascularisation
Open revascularisation
Amputation
Notes: Open revascularisation options include endartectomy and bypass graft

## Slide 42: Bypass graft
Notes: A bypass graft is where less diseased arteries before and after the blocked arteries are exposed and a tube or conduit is sewn to each- blood travels through the conduit and bypasses the blockage, thus restoring blood flow to the lower limb. The conduit is usually taken from the leg using the patients own veins and they come to us first of all to map the veins and help surgical decision making

## Slide 43: Vein mapping for bypass graft
Notes: check the deep veins and then assess the diameters of the superficial veins along their length. We report that and the team decides if a vein is viable. If no veins are suitable then a PTFE graft can be used

## Slide 44: Bypass graft
Notes: We can then provide surveillance for the graft at regular intervals for a year or more if required, here you can see the graft lying within a lower limb- the double lines indicate this is a PTFE graft

## Slide 45: Bypass graft
Notes: We can then provide surveillance for the graft at regular intervals for a year or more if required, particularly if a vein has been used. For us to be able to monitor the quality of the graft and to detect for pending graft failure on top of our usual values we also record the graft flow velocity and ankle brachial pressure index each scan and reductions in both may mean revascularisation of the graft will be required.

## Slide 46: Peripheral Artery Disease
Treatment
Best Medical Therapy + lifestyle advice
Endovascular revascularisation
Open revascularisation
Amputation
Notes: Unfortunately some patients are not suitable candidates for any form of limb salvage or revascularisation, and amputation is the inevitable outcome and w can scan the limb to help guide whether BKA or AKA

## Slide 47: Waveforms
Multiphasic
Monophasic
Triphasic Biphasic
Notes: An important part of our PAD scans involves listening and recording the waveforms- multiphasic is normal and monophasic is abnormal and this is what it looks like on spectral doppler

## Slide 48: Why and when?
Venous Insufficiency
Varicose veins causing venous hypertension.
Notes: The superficial veins can become varicose veins, which are where the valves stop working causing the veins to become larger and balloon up, looking like that bunch of grapes appearance CLICK and meaning blood doesn’t move through the veins effectively increasing the pressure in the veins, this can lead to a range of mild sx such as itching, aching and swelling, and more severe sx which can significantly impact the QoL of patients and include eczema, bleeding and ulcers. (lower leg)
Clinical directed imaging
Imaging should be undertaken with a venous
insufficiency duplex ultrasound scan to assess
for superficial and deep venous reflux. Duplex
means the use of colour imaging to show flow

## Slide 49: Why and when?
Notes: As part of our routine venous investigation we look at all of these veins and these scans can take around 45mins per limb the patient sat on the edge of the couch with their feet on a stool so we can scan from the top of their leg down

## Slide 50: Venous Insufficiency
Artery
Deep Vein
Super-ficial vein
Notes: So first of all we would look at the deep veins and they are analogues of the arteries we’ve just discussed, servicing the same region but returning blood flow. Here in the groin you can see the common femoral artery, common femoral vein and saphenofemoral junction, where the superficial vein drains. Looks like mickey mouse- we call this our mickey mouse sign. We assess the deep veins for patency and flow

## Slide 51: Venous Insufficiency
Notes: Then we look at the superficial veins, which don’t have a corresponding artery and lie within a ksucular fascia and look like an eye- this is our landmar

## Slide 52: Venous Insufficiency
Competent
Notes: So then we assess the blood flow to see if the vales are working. Spectral Doppler of competent valve, for this we squeeze the calf to augment the flow and here is the squeeze, the valve opens and then the valve closes- competent

## Slide 53: Venous Insufficiency
Incompetent
Notes: In diseased veins, one way valves fail to close properly and are incompetent And blood flows back down the leg causing venous hypertension

## Slide 54: Venous Insufficiency
Notes: Generate a report, red indicates incompetent flow/ blue competent. This patient as an incompetent long saphenous vein and calf tributaries

## Slide 55: Venous treatment
Notes: ADD OCCLUDED VEIN REPORT
Change VV report to LSV reflux one

## Slide 56: Venous treatment
Notes: We can provide ultrasound guidance for certain venous treatments, including foam sclerotherapy and RFA where the incompetent veins are targeted- here is a cineloop of a varicose vein being cannulated and injected with foam

## Slide 57: Venous treatment follow up
Notes: Check for DVT, SVT and check how well the treatment has worked. Here is a clip of an occluded long saphenous vein in B-mode and transverse plane and with pressure applied by the transducer to the limb we can see the vein isn’t compressing and is occluded, the treatment was successful.

## Slide 58: Why?
Notes: Well obviously it’s manually intensive nature of the job, glamourous, fragrant, consistent, weird and wonderful, lots of bowel gas issues
No in reality it’s the rapport we build with patients impact we have on patient outcomes

## Slide 59: Why?
Rapport
Patient outcomes
Scientific skill
MDT
Notes: Well obviously it’s the glamour
No in reality, and personally, it’s the rapport we build with patients, our scans can take up to 2 hours sometimes and involving private areas and this really gives us a big insight into their world, and gives us a platform to make a difference through building their trust, education, signposting etc. It’s the positive impact we have on patient outcomes, we see patients throughout their care journeys and on a regular basis. Eg a patient with CTLI- we will diagnose their PAD, then map their veins, see them 1 day post op to check the graft and then 3 monthly for a year. Its using a highly expierenced and specialist scientific skill to diagnose complex disease processes, and of course working in an outstanding MDT

## Slide 60
Vascular Laboratory
GHNHSFT
GRH: 0300 422 5618
CGH: 0300 422 4227
Contact us