## Slide 1: Southmead Hospital Vascular Testing Staff

## Slide 2: Southmead Hospital Vascular Testing
Staff 7 clinical vascular scientists (4FT, 3PT), 2 renal specialist nurses trained to scan fistulas (PT), 1 STP vascular scientist trainee (FT), 3 support workers (PT)
Equipment
  3 large ultrasound machine at Gate 5
  2 mobile ultrasound machine used for ward scanning
Outpatient, hot clinic and one stop scanning done at Gate 5
On-call mobile scanning provided Mon-Fri 0800-1730
Urgent referral please call Ext 45300 or bleep on-call Scientist 9050 or 9051
REFER EARLY AND PHONE TO GARRANTEE SAMEDAY SCAN

## Slide 3: Duplex investigations
Upper and lower limb arterial
Venous incompetence
Upper and lower limb DVT
Fistula
Graft and stent surveillance
AAA surveillance
Pre-operative marking: vein mapping and pre carotid endarterectomy
+ ABPI
Physically demanding especially mobile scans on the ward

## Slide 4: Arterial Duplex
Ultrasound with B-mode, colour flow and Doppler waveform information
  Locate diseased vessels
  Grading of disease to indicate severity of stenosis
  Total occlusion
Level of disease | Degree of stenosis (diameter reduction) | Peak Systolic Velocity Ratio (PSVR)
Minimal disease | 1-10% | No velocity change
Mild disease | 10-49% | Less than 2:1
Mild-moderate disease | ~50% | 2:1
Moderate disease | 50-75% | 2:1 – 3:1
Severe disease | 75-99% | 4:1 or greater
Thread flow | Thread flow | Very low velocity flow. Pre-occlusive vessel.
Occluded | Occluded | No flow

## Slide 5: Graft surveillance
Elective patients have pre-op marking on day of surgery – emergency bypasses can be missed please fill out referral for surveillance
Duplex before discharge very limited
Will highlight concerns in report - scan just a patency check
6 week scan more detailed

## Slide 6: Graft surveillance
Vein graft
  Looks like native vessel
  Retained valves
PTFE
  Uniform diameter
  High echo walls
  Kinking

## Slide 7: Graft surveillance
Graft occlusion
Damped monophasic Doppler signals distal to occlusion

## Slide 8: Graft surveillance
Early pick up of graft stenosis
Complications are highlighted on report and depending on severity email consultant or contact on call registrar/consultant
If graft has intervention radiological or surgical – surveillance re-starts

## Slide 9: Stent Surveillance
Entered into surveillance via referral and MDT outcome list
Scan 6 weeks, 6 months and 12 months
Similar to grafts, complications seen on surveillance reported back to Vascular team and restart surveillance if stent intervention performed

## Slide 10: AAA Surveillance
All AAA surveillance patients are referred vascular team
Placed on surveillance with schedule dependent on size
Inner to inner lumen measurements with small AAA measuring >3cm
When at threshold (≥5.5cm) discharged from surveillance and referred back to vascular surgeon

## Slide 11: AAA Surveillance